## Slide 1: PCMD Biomechanics Core – Learning Lunch
2/15/19

## Slide 2: Biomechanics?
What is the function of…. musculoskeletal tissues (bone, cartilage, tendon, etc)?

## Slide 3: Biomechanics and the MS
To understand normal tissue and joint structure and function
  motion, loads, joint function, locomotion, gait
To understand, diagnose, and treat pathology
  Joint instability, fracture healing, arthritis, osteoporosis, injury
Design and develop implants and devices
  Total joint replacement
  Fracture fixation plates and screws
  Biological treatments

## Slide 4: Fundamental Mechanics Terms/Ideas
Force
Moment
Stress
Strain
Material Properties
Structural Properties
Static Equilibrium
Dynamics
Tension
Compression
Shear
Bending
Torsion
Friction
Wear
Viscoelasticity
Anisotropy
Fatigue

## Slide 5: Stress
Intensity of force (s)
Force / Area
  1 Pa = N/m2
  1 MPa = N/mm2
Specific to a point and a direction in a structure
Takes into account geometry!
F
F
>

## Slide 6: Force vs. Stress
F
Stress = Force / Area = F/A
units = psi, pascals, MPa
Example: Bar in compression
Cross-sectional
Area: A
F

## Slide 7
What Does Force (or Stress) do?
When force is applied to a deformable body it undergoes deformation
Extent of deformation is defined by the properties of that material
The relationship between force (F) and deformation (d) is called the stiffness (S)
d
F
F
S
Undeformed
Deformed
F = S * d

## Slide 8: Strain (e) =
Change in Length (d)
Original Length (LO)
Displacement vs. Strain
10 cm
2 cm
20 cm
2 cm
What happens if we deform two objects by the same amount, but they start with different lengths?
(As with stress, with strain we take geometry into consideration)

## Slide 9
Force-Displacement vs. Stress-Strain
F
F
F
A
C
Displacement
Force
C
B
A
Strain
Stress
A, B, & C
B
Same material, but different apparent stiffnesses
(Structural Properties)
F = S * d
Normalization allows for comparison of samples of different shapes and sizes – Slope is called the modulus (E)
(Material Property)
EY
s = E * e

## Slide 10
Elements of a Stress-Strain Curve

## Slide 11
Material Characteristics
Elastic - Stress is directly proportional to strain and deformation is fully recovered when a load is removed.
Brittle - exhibits a linear stress–strain curve to failure and elastic deformation only (e.g., polymethylmethacrylate, PMMA).
Ductile – materials such as metals undergo a large amount of plastic deformation before reaching failure.
Strain
Stress

## Slide 12
Material Properties
Moduli can be determined in a number of different loading configurations:
  Tension
  Compression
  Shear
  Combinations of the above
Moduli can vary with:
  Deformation state (non-linearity)
  Time (viscoelasticity)
  Direction (tension-compression nonlinearity)
  Direction (anisotropy)

## Slide 13
Linear vs. Non-Linear
Linear Materials
  Modulus is same with any level of deformation
Non-Linear Materials
  Intrinsic to material
  Strain-hardening
  Structurally based (as with tendons/ligaments)
Strain
Stress
Linear
Non-Linear

## Slide 14: Nonlinearity
Phenomenological solution:
s = A[exp(Be)-1]

## Slide 15
Elastic and Viscoelastic Materials
Elastic - Stress is directly proportional to strain and deformation is fully recovered when a load is removed. Elastic materials are insensitive to the rate of loading.
Viscoelastic – stress-strain behavior depends on time and rate of loading. Viscoelasticity is a function of internal friction in the material.
Strain
Stress
Increasing Strain Rate

## Slide 16: Creep and Stress Relaxation
Viscoelasticity (time-dependant behavior) is characteristic of most biologic tissues
  Creep: a constant load is applied and deformation increases with time
  Stress Relaxation: a ramped deformation is held, load increases and then relaxes to equilibrium
Mechanisms
  Friction between matrix molecules
  Drag due to fluid flow and pressurization
  Constitutes energy loss / dissipation
Force
Displacement
time
creep
recovery

## Slide 17: Creep and Stress Relaxation
Displacement
Force
time
Stress
Relaxation
Viscoelasticity (time-dependant behavior) is characteristic of most biologic tissues
  Creep: a constant load is applied and deformation increases with time
  Stress Relaxation: a ramped deformation is held, load increases and then relaxes to equilibrium
Mechanisms
  Friction between matrix molecules
  Drag due to fluid flow and pressurization
  Constitutes energy loss / dissipation

## Slide 18: Creep and Stress Relaxation
Displacement & Force
Stress
Strain
Viscoelasticity (time-dependant behavior) is characteristic of most biologic tissues
  Creep: a constant load is applied and deformation increases with time
  Stress Relaxation: a ramped deformation is held, load increases and then relaxes to equilibrium
Mechanisms
  Friction between matrix molecules
  Drag due to fluid flow and pressurization
  Constitutes energy loss / dissipation
Time

## Slide 19
Confined Compression Stress-Relaxation
0-A-B – Compression (Stress Phase)
B-E – Hold (Relaxation Phase)
Relaxation time dependent on:
Sample Geometry (thickness or radius)
Sample Stiffness
(HA or EY)
Hydraulic Permeabilty
(ko)
Impermeable Wall
Permeable Indenter

## Slide 20: Fluid Pressurization in Articular Cartilage
•
60-85% Water Content
•
Low Permeability (k~10-15 m4/Ns)
•
Load Support (>90%)
•
•
•
Diarthrodial Joints
Soltz and Ateshian, 1998, 2000
W
W
W
W
W
W
Fluid Pressure
Time
Time
Total Stress
Fluid Pressure
Stress (Pa)
Peak Stress
1MPa (~150psi) =17.5 microns/sec fluid flow

## Slide 21: Dynamic Loading of Cartilage
40 hz
10 hz
1 hz
0.1 hz
0.01 hz
Stress (MPa)
Compressive Strain
Faster compressive loading results in a higher dynamic modulus

## Slide 22
Isotropy vs. Anisotropy
Anisotropic material properties vary with the direction of applied load (biologic tissues are mostly anisotropic).
Isotropic materials have the same mechanical properties in all directions.
Strain
Stress
1
2
E1&2
Strain
Stress
E1
1
2
E2

## Slide 23: Fatigue
When subjected to a large number of cycles, materials will fail at a stress lower than the ultimate tensile stress
S-n curve
Endurance
limit